## Slide 1: Botnet Attack Detection at the IoT Edge Based on Sparse Representation
Christos Tzagkarakis
FORTH-ICS

## Slide 2: Introduction
Internet-of-Things (IoT) has advanced the concept of Internet networking
Field/Edge
Network
Backend/Cloud
Smart home
Smart cities
Wearables
Predictive maintenance
Automotive driving

## Slide 3: Introduction
Rapidly growing use and realization of IoT-based technology comes at the cost of resolving business and technical impediments
Focus: efficient, robust and fast detection of botnet attacks at the IoT edge level
Dynamicity
Heterogeneity
Scalability
End-to-end security/privacy
Rapidly growing use and realization of IoT-based technology comes at the cost of resolving business and technical impediments

## Slide 4: Motivation & Background
IoT usage: exponential growth
Autonomous physical/digital objects augmented with sensing, processing and network capabilities
Vermesan and Friess (2014)
Security aspects of IoT devices are often neglected leading to exponential risk
2016 Mirai IoT botnet attack at the US east coast

## Slide 5: Motivation & Background
IoT edge devices typically have limited
power, processing, memory capabilities
IoT gateway might also have similar
technical constraints
IoT-related detection methods focus on early steps of propagation and communication with the C&C server
Network monitoring for early infection identification is not often
sufficient
Develop diagnosis mechanisms when IoT bots begin launching attacks
Last line of defense security layer
Instant detection of IoT botnet attacks
and isolation of compromised IoT devices
Employ fast detection on power constrained IoT devices based on small amount of IoT network traffic data to detect compromised IoT devices

## Slide 6: IoT network traffic data
N-BaIoT dataset
Meidan, et.al, “N-BaIoT: Network based detection of IoT Botnet attacks using
deep autoencoders,” In IEEE Pervasive Computing, vol.13, no.9, July-September 2018
40395
34692
13111
160137
55169
91555
42784
--
46817
Number of benign instances in online dataset
Meidan, et.al, “N-BaIoT: Network based detection of IoT Botnet attacks using deep autoencoders,”

## Slide 7: IoT network traffic data
Data pre-processing: feature extraction
  Whenever a packets arrives, obtain a behavioral snapshot of the hosts and protocols that communicated the packet
  Extract 23 temporal traffic statistics (features/instances) over a temporal window, summarizing the traffic that:
Originated form the same IP
Originated form both the same source MAC and the same IP address
Sent between the source and destination IPs
Sent between the source and the destination TCP/UDP sockets
100 ms
500 ms
1.5 sec
10 sec
60 sec
23 features
23 features
23 features
23 features
23 features
115-dimensional feature instance corresponding to five temporal windows
Meidan, et.al, “N-BaIoT: Network based detection of IoT Botnet attacks using deep autoencoders,”

## Slide 8: Proposed IoT botnet attack detection method
#n1 instances of traffic data
115-dimension
#n2 instances of traffic data
115-dimension
#nS instances of traffic data
115-dimension
Assume IoT devices in general
Instances corresponding to benign traffic behaviour
IoT device 1
sparse code

## Slide 9: Proposed IoT botnet attack detection method
Toy example: ideal sparse code corresponding to a benign instance
Toy example: ideal sparse code corresponding to a
malicious instance
Overall benign data matrix
Observed instance
Time-Delay Embedding
sparsity threshold
Use the concept of reconstruction error to detect abnormality of the sparse codes
Lightweight algorithm
Orthogonal matching pursuit

## Slide 10: Decision threshold estimation
Critical hyper-parameter tuning: decision threshold
We use proxy outliers: based on the computed sparse codes reconstruction errors
Fundamental assumption: we use only benign
IoT traffic data (no malicious training data)

## Slide 11: Decision threshold estimation
We use proxy outliers: based on the computed sparse codes reconstruction errors
Fundamental assumption: we use only benign
IoT traffic data (no malicious training data)
Reconstructed version
matrix V with all
benign “training” instances
RMSE error
Critical hyper-parameter tuning: decision threshold

## Slide 12: Decision threshold estimation
Estimated RMS errors e
Compute the lower quartile Q1
Compute the upper quartile Q3
Compute the inter-quartile range IQR= Q3-Q1
The i-th instance is considered as an outlier (proxy) if
Rejection rate: percentage of instances that are within the non-extreme limits
Threshold set as the maximum value
of the “benign” instances
Hyper-parameter tuning
All benign training data
Proxy outliers estimation
Benign training data
Malicious training data

## Slide 13: Majority voting scheme
100 ms
500 ms
1.5 sec
10 sec
60 sec
window 1
23 instances
window 2
23 instances
window 3
23 instances
window 4
23 instances
window 5
23 instances
solve sparse representation problem for each window separately
majority voting rule
for final decision
Solve the sparse optimization problem for each temporal window separately and use majority voting rule for the final decision
Solve five sparse representation problems act like ensemble learning algorithms to face adverse problem conditions  short training/testing instances
identify if each temporal window’s instance is malicious or benign

## Slide 14: Test case: BASHLITE botnet attack
Examine BASHLITE botnet attack
  Scan: scanning the network for vulnerable devices
  Junk: sending spam data
  COMBO: sending spam data and opening a connection to a specified IP address port
  Positive predictive value (PPV) TP/(TP+FP)
  Sensitivity TP/(TP+FN)
  F1-score (2TP)/(2TP+FP+FN)
  Accuracy (ACC) ((TP+TN)/(TP+TN+FP+FN))

## Slide 15: Test case: BASHLITE botnet attack
3-fold cross validation
Search space of sparsity level {5, 10, 15, 20, 30}
Search space of rejection rate {0.01, 0.5, 1, 2, 3}
Compare sparse representation (SR) vs. typical autoencoder (AE) with a single hidden layer
  Number of epochs 50
  Search space of number of nodes {20, 30, 40, 50, 60}
Leave-one-device-out cross validation (LOOCV)
  Benign instances from S-1 IoT devices are used for hyper-parameter tuning
  S-th IoT device’s benign instances coupled with malicious instances from all other IoT devices are used for performance evaluation
  LOOCV is repeated S times and the average performance is computed
100, 300, 500 benign instances per IoT device for cross validation
1600 total malicious instances from all IoT devices for testing

## Slide 16: Test case: BASHLITE botnet attack
COMBO
Junk
Scan

## Slide 17: Test case: BASHLITE botnet attack
SR achieves superior performance in light of Sensitivity, F1-score and ACC, while AE achieves slightly better results in terms of PPV. That means that SR is robust in accurately detecting both malicious and normal behaviour in the IoT network
The time complexity between SR and AE is comparable and low and thus SR can be applied for accurate and fast IoT botnet attack detection

## Slide 18: Future directions
Examine the efficiency of the proposed approach on more IoT botnet attack datasets and scenarios
Perform thorough comparisons in terms of detection accuracy and time complexity with additional lightweight IoT botnet attack detection methods